## Slide 1
ECG Arrhythmia Classification Using
STFT-Based Spectrogram and Convolutional Neural Network
Presented by:
210169L- W.W.R..N.S. Fernando
210730B- W.M. Wimalasiri
Published in IEEE Access
Authors:
Jingshan Huang, Binqiang Chen, Bin Yao, Wangpeng He.
1

## Slide 2
Cardiovascular Health & Need for ECG Analysis
Why This Matters?
Leading global cause of death
  ~17.7 million deaths per year (~31% of total deaths).
  75% occur in developing countries.
  Key diagnostic tool for monitoring heart rhythm.
  Records excitability, transmission, recovery of heart.
Role of ECG (Electrocardiogram)
Arrhythmia
  Group of abnormal heart rhythms; can occur alone or with other CVDs.
  Critical to detect for prevention & treatment
2

## Slide 3
  Threshold-based methods.
  Digital filters.
  Wavelet Transform (WPD, WT, PCA).
  Entropy measures, AR models, nonlinear features.
Classifiers:
  SVM
  Neural Networks
  Random Forest
  K-NN
  OPF
Introduction & Background
Traditional ECG Classification
Feature Extraction
Pattern Classification
Step 1
Step 2
Limitation
  Require heavy manual feature engineering
  Perform poorly across different patients/devices
  ECG signals are non-stationary, fixed features cannot describe these changes well.
3
Why Look for Something Better
  Need a method that captures both time and frequency variations.
  Need a representation that is deep-learning friendly (automatic feature learning).
  Want to avoid hand-crafted features completely.
Insight That Led to the Solution
  CNNs learn patterns best from images.
  So, if we convert ECG signals → visual patterns, CNNs can detect rhythm differences automatically.
Direction Chose
  Use Short-Time Fourier Transform (STFT) to convert each 10-s ECG window into a time–frequency spectrogram.
  Feed these spectrogram images into a 2D CNN → automatic feature learning.

## Slide 4
Method Overview
  Apply Short Term Fourier Transform to ECG time series 1D data
Transformation into time-frequency spectogram
Proposed ECG arrhythmia classification pipeline
5 heartbeat types:
  Normal (NOR)
  Left bundle branch block (LBB)
  Right bundle branch block (RBB)
  Premature ventricular contraction (PVC)
  Atrial premature contraction (APC)
Classification of Arrhythmias using 2D CNN Classifier
J. Huang, B. Chen, B. Yao and W. He, "ECG Arrhythmia Classification Using STFT-Based Spectrogram and Convolutional Neural Network," in IEEE Access, vol. 7, pp. 92871-92880, 2019, doi: 10.1109/ACCESS.2019.2928017.
4

## Slide 5
Implementation Details
5
Dataset & Preprocessing
Dataset: MIT-BIH Arrhythmia Database
Extracted recordings:
  Choose V5 lead
  make sure the sampling rate is 360Hz
  segment the signals into 10s.
  Do the training and testing set splits from each category
  Total = 2520 samples
  Training set: 2,100 samples
  Testing set: 420 samples
  Balanced across the 5 arrhythmia classes
Notes: V5 lead (or MLII if V5 isn’t available)

## Slide 6
  apply STFT
  Hanning window 50% overlap.
  window size is 512
Implementation Details
6
Dataset & Preprocessing
time domain ECG 10s segments
Time-frequency spectrogram
256 × 256 × 1
Stack all spectrogram tensors into model-ready arrays
train_X_2d and test_X_2d
Convert class labels into one-hot vectors

## Slide 7
Implementation Details
7
Dataset & Preprocessing

## Slide 8
Implementation Details
8
Model Architecture
Input:
  256×256 STFT spectrogram (grayscale)
CNN Feature Extractor:
  Conv(8, 4×4) → MaxPool
  Conv(13, 2×2) → MaxPool
  Conv(13, 2×2) → MaxPool
Classifier:
  Flatten → Dense(64) → Dense(5, softmax)
Total params:
  ~853k (lightweight & fast)

## Slide 9
Results
9
  Fixed learning rate of 0.001
  epochs=100
Notes: To find the best classification performance, we tested the model using several different parameter settings and compared the results.
smaller batch sizes lead to higher validation and test accuracy. In our experiments, batch size 100 achieved the best performance, reaching about 98% validation and test accuracy, which is very close to the paper’s reported accuracy. As the batch size increases, the model’s ability to generalize gradually decreases—batch sizes like 1000 and 1500 fall to the 90–93% range.
The loss and accuracy curves also reflect this behavior: smaller batch sizes converge faster, remain stable, and consistently achieve higher accuracy, while larger batches learn more slowly and reach lower overall performance. Overall, our results successfully reproduce the paper’s results at smaller batch sizes but results have droped in higher batch sizes.

## Slide 10
Results
10
  Fixed learning rate of 0.001
  epochs=100
Our results
Results from paper
Notes: To find the best classification performance, we tested the model using several different parameter settings and compared the results.
smaller batch sizes lead to higher validation and test accuracy. In our experiments, batch size 100 achieved the best performance, reaching about 98% validation and test accuracy, which is very close to the paper’s reported accuracy. As the batch size increases, the model’s ability to generalize gradually decreases—batch sizes like 1000 and 1500 fall to the 90–93% range.
The loss and accuracy curves also reflect this behavior: smaller batch sizes converge faster, remain stable, and consistently achieve higher accuracy, while larger batches learn more slowly and reach lower overall performance. Overall, our results successfully reproduce the paper’s results at smaller batch sizes but results have droped in higher batch sizes.

## Slide 11
Results
11
  Fixed batch size of 100
  epochs=100

## Slide 12
Results
12
  Fixed batch size of 100
  epochs=100

## Slide 13
Results
13
  Fixed batch size of 100
  epochs=100

## Slide 14
Results
14
  Fixed batch size of 250
  epochs=100

## Slide 15
Results
15
  Fixed batch size of 250
  epochs=100

## Slide 16
Analysis
16
  Fixed batch size of 250
  epochs=100
Paper Implementation
Paper Replication

## Slide 17
Results
17

## Slide 18
The best performance was achieved with a batch size of 250 and a learning rate of 0.001, resulting in a learning accuracy of 99.3% and an overall accuracy of 97.3%, with a precision of 97.5%, recall of 97% and F1-Score of 97.2%.
Discussion
18

## Slide 19
  Original paper uses only one STFT window (512 samples).
  A single window cannot capture all ECG events:
    Fast, high-frequency QRS → need small window.
    Slow, low-frequency P/T waves → need large window.
  Result:
    Loss of information → some wave features become blurred.
Proposed Improvement & Implementation
19
Our Proposed Enhancement
Adaptive Multi-Window STFT Front-End
  We compute three spectrograms using window sizes 128, 256, 512.
  These are stacked as a 3-channel (RGB-like) input to the CNN.
Why Multi-Window STFT?
  Each reveals different ECG characteristics.
  Stacking them gives a richer time–frequency representation.

## Slide 20
Results after applying the improvement
20

## Slide 21
Challenges
21
  Insufficient information on the neural network
    Claims the output shapes but cannot obtain those shapes with the given one kernel and maxpooling layer

## Slide 22
Challenges
22
  Inadequate computer resources
    Batch size of 2500 was used in the paper.
    Tried with two T4 GPUs.

## Slide 23
  Hilbert Huang Transform
    Emperical Mode Decomposition- Decomposes a signal into Intrinsic Modes defined by Intrinsic Mode
      ECG signals are non-linear and non-stationary
      Need to extract characteristic components of underlying biological processes
      EMD is fully adaptive, unsupervised and data-driven
      Consider oscillations locally and separate data into locally non-overlapping time-scale components
    Hilbert Transform- to construct a unique analytic signal from a given real signal so
    that instantaneous amplitude and frequency can be analyzed
    Fourier has a constant amplitude and frequency for each sinusoid.
    HHT has a time-varying amplitude and frequency
Possible Improvement
23
One possible Enhancement
Hilbert Transform applied on EMD IMFs

## Slide 24
Possible Improvement
24

## Slide 25
  But, estimating envelopes: over-sampling and cubic splines are costly.
  Therefore, while it may provide accurate predictions, the model would require significant training and inference time.
Possible Improvement
25

## Slide 26
  Furthermore, we explored the use of the Continuous Wavelet Transform (CWT) with the Morlet wavelet, as it provides a sinusoidal kernel rather than a time-limited one, potentially offering more informative time-frequency analysis.
Possible Improvement
26
Morlet wavelet

## Slide 27
Learnings
27
  ECG Arrhythmia Classification performed on five rhythm types:
    Normal beat (NOR)
    Left bundle branch block (LBB)
    Right bundle branch block (RBB)
    Premature ventricular contraction (PVC)
    Atrial premature contraction (APC)
  Model: Deep 2D Convolutional Neural Network (2D-CNN)
  Input Representation:
    Spectrogram images generated using Short-Time Fourier Transform (STFT)
  Best Hyperparameters:
    Batch size: 250
    Learning rate: 0.001
  Future Enhancement:
    Replace standard STFT with an Adaptive Multi-Window STFT

## Slide 28
Thank
You
28